## Slide 1
Enterprise Software Development

## Slide 2: There shall be light: Control LED with your Raspberry Pi and UWP
Jernej Kavka, SSW, Australia

## Slide 3: Why UWP?
C# + XAML
On all Windows 10 platforms
  Desktop, Tablet, Phone, Xbox, IoT, HoloLens, etc.
One app, multiple platforms

## Slide 4: Parts of demo
Step 1
  UWP app with virtual light
Step 2
  Control 1 LED light with IoT extension
Step 3
  Control X LED lights
Bonus step
  Control LED lights with an external service

## Slide 5: GitHub
https://github.com/jernejk/IotHackathonLedDemo
Step-by-step branches

## Slide 6: DEMO - Step 1
UWP app with 1 virtual light

## Slide 7: Step 2
First we need to talk about the basics

## Slide 8: Raspberry Pi 2 pins

## Slide 9: About LED lights
Long leg is +, short one is –
Don’t use LED directly on RPi
  Use resistors (demo uses 4.7k ohm)

## Slide 10: Demo circuit
Pin 1 - 3.3 V power
Pin 39 - GND
Pin 40 – GPIO 21
Pin 38 – GPIO 20
Pin 37 – GPIO 26

## Slide 11: IoT extensions
Use this extension for IoT specific features
  Add references… -> Universal Windows -> Extensions
  Windows IoT Extensions for the UWP
Allows you to access Raspberry Pi pins
  GpioController and GpioPin
Some features are not available on all platforms
  Use ApiInformation.IsTypePresent(fullTypeNameWithNamespaces) to detect features

## Slide 12: DEMO - Step 2
Control 1 LED light with IoT extension

## Slide 13: DEMO - Step 3
Control X LED lights

## Slide 14: DEMO – Bonus step
Control LED lights with an external service

## Slide 15: Sources
https://ms-iot.github.io/content/en-US/win10/samples/KitBlinky.htm
http://fritzing.org/

## Slide 16: Thank you! jernejkavka@ssw.com.au www.ssw.com.au Sydney | Melbourne | Brisbane | Adelaide

## Slide 17: Find me on Slideshare!
http://www.slideshare.net/SSWconsulting